# Project Goals
Improve the Table Lamp in 3 different areas:
- Make it lighter using small screws
- Align the lamp and the base adding a rotating joint to the base
- Add experimental support for CV60 camera
# Dimensions
Base Size: 140x77 mm (it was 140x90 on version 2.0)
Closed Height: 56 mm (it was 75 on version 2.0)
Open height (or Lamp distance from the ground): 480 mm (it was 490 on version 2.0)
Weight: 402! Since it was 494 g on version 2.0, this is a big achievement!

# Images
This is the lamp closed:

And this is the lamp in full swing:

# Components
## Power bank
This is the power bank I have incorporated in the project.

Amazon Germany: https://amzn.eu/d/j4mhf3Z
Amazon Italy: https://amzn.eu/d/agR1Bto

### Why I choose it:
- Because it has a capacity of 10Ah
- Because it has a USB A on one side and USB-C / Micro USB for charging in the opposite side. This make possible the connection with the lamp on one side and leaves the charging connectors available on the other side

## Switching regulator
This small circuit trigger the USB port of the Power Bank and then convert the USB Bus voltage up to 28 VDC. For this application I have adjusted the output to 24VDC.
The input cable is a USB-A, and it has been cut on the other side.

Since the required power consumption is very low (0.76W), I use directly the Bus Voltage (5V) to get the 24VDC for the LED. The resulting input current should be 150 mA.
## LED Strip
I use 2 Modules from 24 VDC COB Led Strip, Natural White. https://amzn.eu/d/dCH8eCl
2 modules => 0,76W

Considering the strip power is 50W/5m, so:
- every module we have: 50W/(5000/38) = 0,38W
- Since I use 2 modules, I have a max power of 0,76W

# Mechanical Elements
The base length is equal to the beam length: 140 mm.
The width is: 28 + 16,5x2 + 16 = 77 mm.
The base height is 28 mm.
The base of the lamp is made in 4 parts to contain the battery, the switch and the electronic board:
- Battery Holder
- Battery Closure
- Battery Cover
- Base Joint
The arm is made by:
- 1 x Dual Axis Beam
- 1 x Long Joint
- 2 x Beams
- 2 x Short Joint
- 1 x Lamp
## Battery Holder
### Top View
The battery holder is created vertically, and the base size is 77 x 28 mm
The charging slot in the center is 15x13 mm and it is located in the center.
The battery compartment is made of 2 x 27 mm cylinders, 33 mm spaced. The circle is curtailed in the top and bottom side.

The battery total length is 82 mm
The top and bottom walls are 1 mm thick.

### Locking slots
On each corner there are 2 slots used to keep the cover and the battery closure in place
They for an L shaped slot, 4.20 x 10.20 mm

### State of charge Display Hole
There is a hole in the top side of the base so the state of charge is visible.
The bottom wall is 1 mm thick.
41.25 is the distance from the USB-A connector
The total height of the battery is 82 mm + 1 mm for the bottom wall.

### Charging slot details
### The charging slot is 15x13 mm large, in the center of the battery bank.

### Battery Holder Resulting 3D layout
The battery holder is printed in Gray and with the charging slot on the bottom.

## Battery closure
This is a cap for the battery compartment and it is used to keep the battery in place, while leaving space for the electronics and wire in the Cover.
The base dimensions are the same as the battery holder: 77 x 28 mm
In the center there is a USB-A 15 x 20 mm connector slot used to plug the electronic board into the power bank.
The locking is possible thanks to 4 pins that are 4x6 mm.

### Battery Closure Resulting 3D layout
This component is printed black to create an edge between 2 gray parts.

## Battery Cover
### Rotating Joint Lock

### Electronics

### Assembly

## Base Joint
Printing this part using PETG was unsuccessful because the resulting part was brittle and cannot withstand the mechanical stress of the hinge.
I solved it increasing the extrusion temperature close to the maximum. The resulting part is very resistant.
## Double Axis Beam
## Long Joint
## Beam
## Short Joint
## Lamp

### CV60 Camera Holder

### CV60 Camera mechanical dimensions.

# BOM
## Nuts and Bolts
For the battery compartment to lock the arm joint that allows the rotation
M3x14 mm Bolts used	2
For the arm:
- M3 x 25mm Cylindrical Head Screws	7
- M3 Nuts	7
Power:
- Power Bank
- USB to 24VD step-up converter
- USB A to C Cable
- Power Switch
- LED Strip
- 1/4-20 UTF Screw for the Manfrotto Telephone Holder
- 2 x 0,13 red and black cable: 1 mt

## 3D Printer Layout – Black

## 3D Printer Layout – Gray

## 3D Printer Layout – White
We need support to print correctly this parts.
This is faster and create better results than printing the lamp vertically.

## 3D Printer Layout – Black – Camera Holder

# Suggestions for next iteration
## Base Interlock improvements
Find a better way to lock the three components of the base. Currently I use some black electric tape and it is enough, but I think there can be a better solution that guarantee that we can remove the power bank without any tools and in the same time the base is locked.
## Weight reduction
Additional weight reduction can be achieved working on the base and using a less resistant structure. But the gains we can get are maximum around 50 gr. In any case this means a final weight below 400 gr.
3MF File	Simulated Weight [g]
Table Lamp 3.0 BlackComponents-ReadyToPrint	43,86
Table Lamp 3.0 GrayComponents-ReadyToPrint	93,69
Table Lamp 3.0 JointHolder-ReadyToPrint	4,67
Table Lamp 3.0 WhiteComponents-ReadyToPrint	36,01
Table Lamp 3.0-BaseJoint-ReadyToPrint	5,79
	184,02
Power Bank	200

Many walls in the base can be shrunk from 2 mm to 1 or from 1 to 0.8.

## Stability improvements
Add 4 Feet can improve the stability. The power bank in the center can create a little bulge.
## Arm improvements
The base joint can be smaller and made for 16 mm. This will save the enlargement to 20 mm. / This lead to a 4 mm reduction in the base width (from 77 to 73 mm)

## Colors
There are a few suggestions that need to be tested
- All White with Black Switch, black power bank (covering the orange / green ring), black battery cover.
- All White and battery cover aligned with the ring color (green / orange)
- All green, with Orange insert to match the power bank SOC Ring and a white insert in the lamp.
- JuventusFC / INTER FC style / Milan FC style

## Lamp improvements
### More light power
Add a second strip in order to have twice the light
### Touch Dimmer
Add a touch dimmer to control the light intensity