# Table Fan
I get some PC fans scraping an old project and I decide to wire it with a USB Power Bank to create a portable fan

## Use Cases:
Summer heat relief
Soldering Iron Fumes dispersion

# Components
## PC Fan
Size:	70 x 70 mm
Mounting:	60 x 60
Voltage:	12 VDC
Power:	0.7 W

# Mechanical parts
## Battery Holder
Width: 77 mm
this has to align to the base jont size.
67 mm + 5 mm + 5 mm

Wall Thikness: 1 mm for all sides
In past realization I use 2 mm for the side, but it is not neccessary

Back Window: width 11 height 13, 4,5 mm offset on the micro USB connector side.
This is used to charge / discarge the battery using USB-C or Micro USB connector

Battery housing: 2 x 27 mm circles, spaced by 33 mm, with a cut at 25 mm on top and bottom side.
The exact shape is difficult to guess, but this is a good approximation and it keeps the battery locked.

Cover Anchor: I use 4 L shaped slots that has also the fuction of saving material.
This slot generate a T shaped beam on the side of the battery holder, that make it stiff and resistent.

State of charge Indicator: On the top side the SOC indicator is visible
The indicator is aligned to the vertical axis and it is 41.25 mm away from the top side

## Battery cover
This is a 2 mm thickness layer that cover the battery and hold it in place.
4 Stub with an extrusion height of 10 mm are used to hook the cover to the battery holder
4 slot are used to allow the hooks of the Electronic Section to pass through.
The 15 x 20 mm slot in the center is used by the USB A connector that power the fan
2 Additional 12 x 5 mm slots, in the horizontal symmetry axis are used to facilitate the cover extraction while in place.

## Cover
This is the part of the base where the fan is connected and where there is the switch

# More Ideas
Can I create a Table Air Purifier?
https://amzn.eu/d/5t24OPc

# For next Iteration
Use 4 wires fan, so we can use PWM to control speed