# Project Goals
Improve the Table Lamp in 3 different areas:
- Make it lighter using small screws
- Align the lamp and the base
- Add support for CV60 camera using an Heat Set Insert
# Dimensions
Base Size: 140x77 mm (it was 140x90 on version 2.0)
Closed Height: 56 mm (it was 75 on version 2.0)
Lamp distance from the ground: 480 mm (it was 490 on version 2.0)
Weight: 494 g (it was on version 2.0)
# Images

# Components
## Power bank
This is the power bank I have incorporated in the project.

Amazon Germany: https://amzn.eu/d/j4mhf3Z
Amazon Italy: https://amzn.eu/d/agR1Bto

### Why I choose it:
- Because it has a capacity of 10Ah
- Because it has a USB A on one side and USB-C / Micro USB for charging in the opposite side. This make possible the connection with the lamp on one side and leaves the charging connectors available on the other side

## Switching regulator
This small circuit trigger the USB port of the Power Bank and then convert the USB Bus voltage up to 28 VDC. For this application I have adjusted the output to 24VDC.
The input cable is a USBA to Micro USB cable.

Since the required power consumption is very low (0.76W), I use directly the Bus Voltage (5V) to get the 24VDC for the LED.
The resulting input current should be 150 mA.
## LED Strip
I use 24 VDC COB Led Strip, Natural White => 0,76W

I use 2 sections, the power is 50W/5m, so:
- every module we have: 50W/(5000/38) = 0,38W
- Since I use 2 modules, I have a max power of 0,76W

# Mechanical Elements
# Base

Length is equal to the beam length: 140 mm
Width: 28 + 16,5x2 + 16 = 77 mm
Height: 1 mm base wall + 80.5 mm

## CV60 Camera Holder

### CV60 Camera mechanical dimensions.

# BOM
## Nuts and Bolts
For the battery compartment to lock the arm joint that allows the rotation
M3x14 mm Bolts used	2
For the arm:
- M3 x 25mm Cilindrical Head Screws	7
- M3 Nuts	7
Power:
- Power Bank
- USB to 24VD step-up converter
- USB A to C Cable
- Switch
- LED
- UTF Screw for the Manfrotto Telephone Holder

# Suggestions for next iteration
Find a better way to lock the three components of the base. Currently I use some black electric tape and it is enough, but I think there can be a better solution that guarantee that we can remove the power bank without any tools.

Additional weight reduction can be achieved working on the base and using a less resistant structure. But the gains we can get are maximum around 50 gr.
3MF File	Simulated Weight [g]
Table Lamp 3.0 BlackComponents-ReadyToPrint	43,86
Table Lamp 3.0 GrayComponents-ReadyToPrint	93,69
Table Lamp 3.0 JointHolder-ReadyToPrint	4,67
Table Lamp 3.0 WhiteComponents-ReadyToPrint	36,01
Table Lamp 3.0-BaseJoint-ReadyToPrint	5,79
	184,02

4 Feet can improve the stability