# Project Goals
Improve the resulting product in 3 direction:
- Packaging: make the closed lamp more compact and suitable for transportation
- Energy: use a more powerful power bank (from 5Ah to 10 Ah)
- Flexibility: add a few fixture to attach cameras or phones.
- Add Self Locking Nuts for better control of frictions along hinges

Additional feature:
Add a threaded bolt for UNC ¾ screw for Manfrotto mounting for Mobile Phone

# Dimensions
Base Size: 140 x 90 mm
Closed Height: 75 mm
Total Height: 490 mm
Weight: 494 g

# Images
Below a set of images of the assembled lamp
Closed, ready for transportation

Open, in use

State of charge Indicator and power switch detail	Recharge / Power Output detail

# Components
## Power bank
This is the power bank I have incorporated in the project.

Amazon Germany: https://amzn.eu/d/j4mhf3Z
Amazon Italy: https://amzn.eu/d/agR1Bto

### Why I choose it:
→ Mainly because it has a USB A on one side and USB-C / Micro USB for charging in the opposite side.
This make possible the connection with the lamp on one side and leaves the charging connectors available on the other side

## Switching regulator
This small circuit trigger the USB port of the Power Bank and then convert the USB Bus voltage up to 28 VDC. For this application I have adjusted the out to 24VDC

## LED Strip
I use 24 VDC COB Led Strip

## Nuts and Bolts
The project requires also
For the battery compartment:
2 x M3x16 mm Bolts used
For the arm joint to be fixed to the base:
6 x M3x16 mm Bolts used
For the arm:
7 x M6x30 mm Bolts
14 x 6 mm washers
7 x M6 Self Locking Nuts

# Mechanical Elements
## Base
The base is made in 3 parts to contain:
- Power bank
- Switch
- Power circuit
### Battery Power Bank Dimensions
The battery pack has the following dimensions:
64 mm width (60 +2+2 mm)
29 height (27 + 1+1 mm)
81.5 length

### State of charge Display Hole
There is a hole in the top side of the base so the state of charge is visible.
Considering a wall size of 1 mm
41.75 is the distance from the USB-A connector

### Power Switch Slot dimensions
Below the dimensions for the slot used to fix the power switch

## Cover

## Base Joint
## Long Joint
## Small Joint

## Double Axis Beam

## Beam
There are 2 identical beams. These are main dimensions
Section: 20 x 16 mm
Holes: 6.20 mm
Lenght: 170 mm
Cable Passage: 3 x 4 mm

The cable passage moves from one corner to the other

Beam Slot

## Lamp

## Base Joint

\

## Base Mounting Screws

## Battery closure