FS40 Pivot Bracket

# Camera drawings

# Adapter Plate
This plate is to connect to the camera side to the bracket creating a hinge centered around the camera optical axis

The bracket is symmetric and has twice the needed M3 holes just to use the same plate on both sides.

# Base

Final result

# Shoulder

The pivot is made with 2 angles so the camera wouldn't fall down even with the brackets in vertical position. Two small teeth act as a stop block.
Embossed text indicate the rotation angle

# BOM
- M3 x 20 Screws:	6
- M3 x 10 Screws:	4
- M6 x 10 Screws:	4
- 6mm washers:	2