Ceiling Lamp

# Project Goals
Create a light using a Recessed Ceiling LED Led.
The lamp is made by 2 body:
- Lamp Base: this is fixed to the wall or to the ceiling
- Lamp Case: this is the removable part where the Recessed LED Light is mounted.
The 2 body are connected with a thread, like a jar and his cap.
The resulting object is quite big the 2 part can be printed in one go.
This is the first project where I use 3D Printed threads.

# Reference
These are the Recessed LED Lights I have used for the project.
https://amzn.eu/d/hiAGEYF

## Recessed LED Lamp Size

Diameter: 72 mm
Maximum diameter: 98 mm
Height: 50 mm

# Drawings: Lamp Base
The outer diameter is 125 mm
The outer wall is 6 mm thick to accommodate the thread.
There are 12 slots on the side that are used to vent out the heat generated by the lamp.

# Drawings: Lamp Case
This is the case for the recessed LED light.
The maximum external diameter is 140 mm

# 3D Model: Lamp Base
The base thickness is 3 mm. The big hole in the center is used to accommodate the plastic tube with wires.
The wall height is 25 mm

## Side wall thread
The side thread is metric, 15 mm high and M125x8 mm.
In order to have a smooth coupling, the thread surface are recessed by 0.2 mm.

This is how the thread looks like using an section inspection.

# 3D Model Lamp Case
Extrusion:
- Base 3 mm
- Body 5 mm
There are 4 parts that moves from outside to inside and are used to keep the recessed LED centered.

## Threads
0,3 for Fillet and for offset of all faces of the male thread

# 3D Printing
## Export configuration
To achieve a good print quality it is mandatory to configure the export dialog for a high level of refinement.

## Ready to print layout

# Appendix
## Reference about using Fusion 360 and Threads
https://www.youtube.com/watch?v=aGWrFeu8Hv0
3D Printed Threads - Model Them in Fusion 360 | Practical Prints #2