FS80 Bracket

# Project Goals
Create a support bracket than can simplify the test of an FS80.
The bracket is not intended for field installation but only for short term lab test.
# Mounting Drawings

# Design
## FS80 Bracket
Mounting Screws: 4x 4 mm diameter / 6 mm length

Support Pin: Diameter 5.8 mm, height 7 mm

## FS80 Shoulder
Center slot 6 mm
Locking screw: 6 mm x 10 mm dept

We need 2 of this shoulder.
## FS80 Bracket Base
Mounting screws: 6x 3 mm diameter x 16 mm long

# Components Pictures

# For Next iteration
Temperature resistance of the bracket need to be validated.
Maybe a different connection between the camera body and the flange can shield the bracket for excess temperature.
The text in the graduation area has a poor readability. Try to double the size and use only half number of labels.