Ceiling Light

# Project Goals
Create a light using a Recessed Ceiling LED Led.
Create the lamp using 2 body that can be screwed one inside the other.
The resulting object is quite big and can be complicated to print and it can use a lot of filament.
And this is the first project where I use 3D Printed threads.

# Reference
These are the Recessed LED Lights I have used for the project.
https://amzn.eu/d/hiAGEYF

## Recessed LED Lamp Size

Diameter: 72 mm
Maximum diameter: 98 mm
Height: 50 mm

# Drawings Lamp Case
This is the case for the recessed LED light.
The maximum external diameter is 140 mm

# 3D Model Lamp Case
Extrusion:
- Base 3 mm
- Body 5 mm
There are 4 parts that moves from outside to inside and are used to keep the recessed LED centered.

## Threads
0,3 for Fillet and for offset of all faces of the male thread

## Reference
https://www.youtube.com/watch?v=aGWrFeu8Hv0
3D Printed Threads - Model Them in Fusion 360 | Practical Prints #2

# 3D Models

# Log
Provo a fare il case da 120 con parete di 5 mm in modo da migliorare la posizione delle molle di aggancio
Faccio il bordo stondato
Provo ad impostare la finitura alta in modo da non vedere I segmenti del poligono
Per creare un filetto ricordarsi di selezionare il flag modella

Per il filetto tra corpo e base ho usato
Lato Femmina
- 0.30 smusso gola interna
- 0.30 smusso cresta esterna
Lato Maschio
- 0.2 offset 3 faccie della cresta
- 0.30 smusso cresta

2025-01-07
Provo con 140 mm per permettere estensione lamelle
Rimuovo canali di scarico calore (che vanno fatti nella base)
Lato Femmina
- 0.30 smusso gola interna
- 0.30 smusso cresta esterna
Allargo il foro del faretto da 75 a 85 per facilitare inserzione
Ho messo anche 2 tacche a 75 mm di diametro altrimenti balla

Lato Maschio
- 0.2 offset 3 faccie della cresta
- 0.30 smusso cresta