# Project Goals
Improve the Table Lamp in many different areas:
- Make it lighter using better design
- Improve the dual axis beam to make the lamp smaller
- LAMP
  - Double the light power using 2 LED strip side by side
  - Add a touch dimmer to the lamp block, so it is always visible
  - Add a lamp screen using Policarbonate
  - Add a rotating joint to the lamp block so we can orient the emission plane. Currently, when the lamp is deployed it gets some strange angles.
  - Remove the Manfrotto Fixture
  - Remove the CV60 Hook
- Improve the color and the final layout
- Add four feet to the base in order to improve stability
Project management
Use a different project development approach: create a file for each object and then merge all together to simulate the total structure.

# SAL
### Completati
- Lamp Light Cover
- Lamp Body
- Lamp Strip
- Lamp Skirt
- Lamp Orientation Joint
- Arm-Long-Joint
- Arm-Short-Joint
- Arm Base Joint
- Arm-Dual-Axis-Beam
- Base-Joint-Lock
- Base-Battery Cover
### Da fare
Stampare skirt e strip in bianco
Cambiare inserimento e metterlo a 90° (e se lo scavo fosse 0,75?)
con 0.75 funziona bene
Update Base Cover
- Tornare a 2 mm
- Togliere 2 mm per recuperare allungamento battery holder
- Spostare slot per cacciavite via dal piolo di bloccaggio
Fare disegno base cover con perno rotazione base
Serve il joint lock

Base Joint: allargare la finestra per il cavo
→ Modificato Ristampare
Migliorare il double axis per il passaggio cavo lato base
In stampa
Ristampare Policarbonato che si è rovinato
→ Bisogna seccare il policarbonato – in forno
Fare il disegno del beam
Lanciata la stampa, da verificare
Non va bene, manca uno scasso su una cerniera
Fare stampa dei Blu per provare ad unire con il grigio
Non è male! Quella per Mario la faccio così
Provare a stampare I giunti in grigio per vedere che effetto fa con il blu

Finire Battery Holder
Passare a 28 mm di spessore
Aggiungere 2 mm di parete per agganciare meglio il coperchio
Disegnare spigoli per forzare aggancio
0.5 è troppo, provo 0.25 – funziona, ma non è adatto allo smontaggio, gli spigoli si rovinano
Rivedere la base
Base Joint Lock
Avvicinare I 2 fori di 1 mm (da 8x2 a 7.5x2)
Fatto – stampa in corso - perfetto
Agganciare Battery Holder nel Cover, non il contrarioCreare due assi con 2 blocchi che possono schiacciare per sbloccare
Battery Holder
Nuovo Aggancio al Cover
Provare a togliere mezzo millimetro alla batteria
Battery cover:
agganciato al cover, non sui bordi ma in centro
Stampa in corso con nuova gola di ancoraggio
Meglio fare solo un lato, il lato in appoggio non esce bene con uno sbalzo di 2 mm, resta un profilo sporco.

### Da comperare
Accessori
Piastra PEI liscia in bambù
31

Ricarica PLA
Nero 10101
Giallo 10400
Arancione 10300
Giada Bianca 10100
68

Bobinati PLA
Verde Bambu (10501)
Blu 10601
Grigio 10103
Rosso 10200
80

Totale	179
Pago in 3 Rate	59,67

## Components
### Lamp Dimmer
https://www.aliexpress.com/item/1005005093284439.html

## Mechanical Components
### Lamp
2 mm il fondo
5 mm di estrusione
3 mm di basetta
6 mm di skirte

# For next iteration
Add a Qi Charger port
Remove switch, I can use the one from the power bank
Modify the Lamp to consider the 0.5 mm for the cover
The cable tie cannot fit, find a different way to lock the power cable in place
The 2 axis beam is printed on the printing plate and this make it different from the others when the lamp is closed
Find a different way to create the cable passage to avoid cable accumulation