# Project Goals
Improve the resulting product in 3 direction:
- Packaging: make the closed lamp more compact and suitable for transportation
- Energy: use a more powerful power bank (from 5Ah to 10 Ah)
- Flexibility: add a few fixture to attach cameras or phones.
- Add Self Locking Nuts for better control of frictions along hinges

# Dimensions
Base Size: 140 x 90 mm
Closed Height: 75 mm
Total Height: 490 mm
Weight: 494 g

# Images
Below a set of images of the assembled lamp

# Components
## Power bank
This is the power bank I have incorporated in the project.

Amazon Germany: https://amzn.eu/d/j4mhf3Z
Amazon Italy: https://amzn.eu/d/agR1Bto

### Why I choose it:
→ Mainly because it has a USB A on one side and USB-C / Micro USB for charging in the opposite side.

## Switching regulator
This small circuit trigger the USB port of the Power Bank and then convert the USB Bus voltage up to 28 VDC. For this application I have adjusted the out to 24VDC

## LED Strip
I use 24 VDC COB Led Strip

## Nuts and Bolts
The project requires also
6 x M3x16 mm Bolts
7 x M6x30 mm Bolts
14 6 mm washers
7 Self Locking Nuts

# Elements
## Base
## Battery Pack
64 mm width (60 +2+2 mm)
29 height (27 + 1+1 mm)
81.5 lenght

## Cover

### Switch

Display Hole
Considering a wall size of 1 mm
41.75 is the distance from the USB-A connector

## Base Joint
## Long Joint
## Small Joint
## Double Axis Beam
## Beam
20 x 16 mm
Holes: 6.20 mm
Lenght: 170 mm

## Lamp

## Base Joint

\

## Base Mounting Screws

## Battery closure