# Multi Camera mount (3 cameras 1 Clamp)
## Back Side camera bracket

### Mounting screws

I set the thickness to 4 mm so I can use M3 x 8 mm and a washer.
→
# Multi Camera mount 2.0 (3 cameras 1 Clamp)
Improvements:
- Better alignment of the beam and the mounting plate
- Rounded mounting plates (10 mm radius)
## Camera Plate
I add 4 R10 circles to round the plate and make it smooth
Changed the side mounting holes with a 16 mm rounded flange to better adapt to the beam

## Support Beam
Total length: 288,40 mm
Camera distance: 96,20 mm

## Printing layout

## Final result (2.0)

Camera plate mounted to the camera

## Possible improvements
The rounding diameter is not ok, better try with a lower radius (current radius is 10 mm)

# Multi Camera mount 1.0 (3 cameras 1 Clamp)
## Support Beam
2 x 6 mm screws for each camera → 6 Screws
2 x 6mm washers for each camera → 6 Washers

## Camera Plate
Thickness: 4 mm

## Top view

## Final result
## Possible improvements
### Camera mount
Since the camera is rounded, so should be the camera mount. Having it squared makes it ugly

### Beam and camera mount joint
The beam is 16 mm wide, the mounting fixture is 12 mm wide, hence this give an impression of mismatching