FS40 Pivot Bracket

Version 2.0

# Version 2.0
- Rotation angle expanded
- Fixed an issue with the text on one side (but the resulting text has a poor quality)
- Larger 8.2 hole in the base
# Camera drawings

# Adapter Plate
This plate is to connect to the camera side to the bracket creating a hinge centered around the camera optical axis

The bracket is symmetric and has twice the needed M3 holes just to use the same plate on both sides.

# Base

Final result

# Shoulder
Version 2.0: larger rotation angle thanks to more locking holes. Now we can rotate from -45° to 120°

This is the detail about the locking holes

The pivot is made with 2 angles so the camera wouldn't fall down even with the brackets in vertical position. Two small teeth act as a stop block.

Embossed text indicate the rotation angle (but the result is not satisfactory)

# BOM
- M3 x 20 Screws:	6
- M3 x 10 Screws:	4
- M6 x 10 Screws:	4
- 6mm washers:	2

# Final result