# Project Goals
Improve the Table Lamp in 3 different areas:
- Make it lighter using small screws
- Align the lamp and the base
- Add support for CV60 camera
# Dimensions
Base Size: 140x77 mm (it was 140x90 on version 2.0)
Closed Height: 56 mm (it was 75 on version 2.0)
Lamp distance from the ground: 480 mm (it was 490 on version 2.0)
Weight: 402! Since it was 494 g on version 2.0, this is a big achievement!

# Images
This is the lamp closed:

And this is the lamp in full swing:

# Components
## Power bank
This is the power bank I have incorporated in the project.

Amazon Germany: https://amzn.eu/d/j4mhf3Z
Amazon Italy: https://amzn.eu/d/agR1Bto

### Why I choose it:
- Because it has a capacity of 10Ah
- Because it has a USB A on one side and USB-C / Micro USB for charging in the opposite side. This make possible the connection with the lamp on one side and leaves the charging connectors available on the other side

## Switching regulator
This small circuit trigger the USB port of the Power Bank and then convert the USB Bus voltage up to 28 VDC. For this application I have adjusted the output to 24VDC.
The input cable is a USBA to Micro USB cable.

Since the required power consumption is very low (0.76W).
I use directly the Bus Voltage (5V) to get the 24VDC for the LED.
The resulting input current should be 150 mA.
## LED Strip
I use 2 Modules from 24 VDC COB Led Strip, Natural White. https://amzn.eu/d/dCH8eCl
2 modules => 0,76W

I use 2 sections, the power is 50W/5m, so:
- every module we have: 50W/(5000/38) = 0,38W
- Since I use 2 modules, I have a max power of 0,76W

# Mechanical Elements
The base length is equal to the beam length: 140 mm, the width is: 28 + 16,5x2 + 16 = 77 mm and the base height is 29 mm.
The base of the lamp is made in 3 parts to contain:
- Battery Holder
- Battery Closure
- Battery Cover
- Base Joint
The arm is made by:
- 1 x Dual Axis Beam
- 1 x Long Joint
- 2 x Beams
- 2 x Short Joint
- 1 x Lamp
## Battery Holder
## Battery closure
## Battery Cover

## Base Joint
Printing this part using PETG was unsuccessful because the resulting part was brittle and cannot withstand the mechanical stress of the hinge.
I solved it increasing the extrusion temperature close to the maximum. The resulting part is very resistant.
## Double Axis Beam
## Long Joint
## Beam
## Short Joint
## Lamp

### CV60 Camera Holder

### CV60 Camera mechanical dimensions.

# BOM
## Nuts and Bolts
For the battery compartment to lock the arm joint that allows the rotation
M3x14 mm Bolts used	2
For the arm:
- M3 x 25mm Cylindrical Head Screws	7
- M3 Nuts	7
Power:
- Power Bank
- USB to 24VD step-up converter
- USB A to C Cable
- Power Switch
- LED Strip
- 1/4-20 UTF Screw for the Manfrotto Telephone Holder
- 2 x 0,13 red and black cable: 1 mt

## 3D Printer Layout – Black

## 3D Printer Layout – Gray

## 3D Printer Layout – White
We need support to print correctly this parts.
This is faster and create better results than printing the lamp vertically.

## 3D Printer Layout – Black – Camera Holder

# Suggestions for next iteration
## Base Interlock improvements
Find a better way to lock the three components of the base. Currently I use some black electric tape and it is enough, but I think there can be a better solution that guarantee that we can remove the power bank without any tools and in the same time the base is locked.
## Weight reduction
Additional weight reduction can be achieved working on the base and using a less resistant structure. But the gains we can get are maximum around 50 gr. In any case this means a final weight below 400 gr.
3MF File	Simulated Weight [g]
Table Lamp 3.0 BlackComponents-ReadyToPrint	43,86
Table Lamp 3.0 GrayComponents-ReadyToPrint	93,69
Table Lamp 3.0 JointHolder-ReadyToPrint	4,67
Table Lamp 3.0 WhiteComponents-ReadyToPrint	36,01
Table Lamp 3.0-BaseJoint-ReadyToPrint	5,79
	184,02
Power Bank	200

Many walls in the base can be shrunk from 2 mm to 1 or from 1 to 0.8.

## Stability improvements
Add 4 Feet can improve the stability. The power bank in the center can create a little bulge.
## Arm improvements
The base joint can be smaller and made for 16 mm. This will save the enlargement to 20 mm. / This lead to a 4 mm reduction in the base width (from 77 to 73 mm)

## Colors
There are a few suggestions that need to be tested
- All White with Black Switch, black power bank (covering the orange / green ring), black battery cover.
- All White and battery cover aligned with the ring color (green / orange)
- All green, with Orange insert to match the power bank SOC Ring and a white insert in the lamp.
- JuventusFC / INTER FC style / Milan FC style

## Lamp improvements
### More light power
Add a second strip in order to have twice the light
### Touch Dimmer
Add a touch dimmer to control the light intensity